## Slide 1: Autonomous Agents Networks
Akraino Physical AI Blueprint Family, v0.1

## Slide 2: Contents
Overview – Agents, Machines, and Interaction
Motivation
  autonomous agents are the next industrial revolution
  prioritize communication, collaboration, and human safety
Agent-Agent Interaction
  use cases
  cloud independent
Human-Agent Interaction
  use cases
  safety is a primary concern
Key Technologies
  P2P communication over cellular and satellite networks
  small multimodal models
    human interaction - audio and visual
    environmental recognition – hazards and dangerous conditions
    small form-factors pose performance challenges
Hardware Examples
Software Components
  Kaldi or Whisper ASR
  OpenCV
  Mediashark
  small multimodal models – Llama-4, Gemma 3, Qwen2, MiniPCM

## Slide 3: Overview – Agents, Machines, and Interaction
“Agents” vs “Machines”
  agents imply autonomy, goal-orientation, and ability to learn and adapt
  as agents become more flexible, like humans they will be separate from machines, for example a car might have a humanoid robot driver (even if the car has its own automation)
  there is some risk in using the term “agents”, as “machines” will inevitably become a popular term
  specific use cases may refer to “machines”
“Interaction” includes …
  bi-directional communication, feedback
  fundamentals of collaboration – situational awareness, reaction, teamwork
Univ of Tokyo, Kento Kawaharazuka

## Slide 4: Motivation
In the next industrial revolution agents must …
  collaborate with each other and with humans
  operate fully autonomously, with intermittent cloud connectivity when available
    expectations of always-available cloud connectivity are unrealistic, expensive, not secure, energy hungry – and most importantly – unsafe
  maximize energy efficiency, resilience, and adaptability
    the correct approach to distributed intelligence, as demonstrated by evolution
Agent collaboration and human safety are top priorities
  human safety is the most difficult challenge
  open source software, small form-factor hardware, new DNN 1 training methods, and 3GPP and IEEE P2P communication standards are emerging areas of innovation
BigAI business models and product incompatibility are problematic
  they will make less money when intelligence is decentralized
  not their top priority
4th Industrial Revolution is the 2nd Information Revolution [Surajudeen Abiola Abdulrahman, MD, MHPM, PhD, National Health Service, UK]
4th Industrial Revolution includes human interaction with digital devices [Neos Networks, https://neosnetworks.com/resources/blog/what-is-fourth-industrial-revolution-4ir]
1 Deep Neural Network

## Slide 5: Autonomous Agents Networks Blueprint
AAN is a member of the Akraino Physical AI blueprint family
  agents are robots, drones, automated vehicles, factory fixed and mobile, environmental sensors
  agent-agent and human-agent interaction
  cloud independence and human safety are primary objectives
  two (2) key underlying technologies are AI and telecom
Initial use cases
  Industrial Collaboration
  Flood Detection, Prediction, and Rescue
  First Responder Machine Assistants

## Slide 6: Agent-Agent Interaction
Industrial use cases
  manufacturing
  mobile delivery and roadside (cleaning, driver assistance)
  construction
  agriculture
Peer-to-peer communication over cell and satcom networks
  unreliable or unavailable cloud connection
  3GPP C-V2X (+ PC5 sidelink and relay), IEEE 802.11x DSRC1, LoRa P2P
  short, low-power, codified messages
  multicast to other agents in close proximity
  optional audio, video, and text description, depending on agent processing capabilities
Sidelink
1 Dedicated Short Range Communications

## Slide 7: Human-Agent Interaction
Use cases
  flood prediction, detection, and rescue
  first responder machine assistants
  proximate machine safety
Audio and visual interaction
  small multimodal models
  unreliable or unavailable cloud connection
  very small form-factor devices (e.g. pico ITX)
  background noise, urgent or stressed voice input, and background talkers
  machine noise from servo motor and other mechanical sources
Excerpt from Amazon delivery drone patent

## Slide 8: Key Technologies
Telecom
  P2P communications over cell and satellite networks
  short, energy-efficient, machine-readable messages prioritized by human safety, commercial need, machine failure, etc
AI
  small multimodal models, recognizing
    speech, behavior, and gestures
    hazards and dangerous conditions

## Slide 9: Technology Challenges
Severe SWaP 1 constraints
  small size, especially in drone and consumer applications
  low power consumption, posing a technical challenge for communication and small multimodal models
  weight is limited and may have less obvious consequences, for example GPU use may be limited due to heatsink of liquid cooling requirements
Model performance and accuracy
  limited number of CPU cores
Data storage
  dedicated storage nodes may be required
1 Size, weight, and power consumption

## Slide 10: Hardware Examples
Very small form-factor
  under 15 W, battery powered for 2 - 6 hours
  4 x 3”, heat sink only, no fans
Operate as small servers
  standard Linux OS (Ubuntu, Debian, etc), command line
  in the lab connect a keyboard and display
  open source development and test support
Pico ITX quad-core Atom x86 server, Ubuntu boot
Pico ITX 6-core Arm server, Debian boot

## Slide 11: Supplemental
Following slides are FYI only, from related or previous presentations

## Slide 12: Use Cases
Factory floor personnel giving urgent commands
  possibly dangerous equipment (e.g. forklifts)
  hands-free environments (e.g. food processing)
First responders communicating with disabled or disconnected robotic vehicles
  robotaxis
  cargo trucks
Language Translation
  independent of ASR model and language model

## Slide 13: Precise Command Problem
Machine-readable APIs must be precise
Minimizing false positives is crucial
Under difficult conditions, efficient open source ASRs such as Kaldi and Whisper produce "sound-alike“ errors, for example: “in the early days a king rolled the stake” which must be corrected to “in the early days a king ruled the state”
Sound-alike errors are problematic for safety and emergency situations
  Internet / cloud connection cannot be assumed. Phones may be useless
  for a robotaxi, a first responder may use a portable hand-held device and give general, conversational such as "get off the road up ahead there and shut down“
  sometimes labeled in ASR research as “substitution errors”
Prediction and decision boundary line is always hard to define 1
1 https://medium.com/@Sanskriti.Singh/an-emphasis-on-the-minimization-of-false-negatives-false-positives-in-binary-classification-9c22f3f9f73

## Slide 14: Current SLM State-of-the-Art
Currently Llama-2 7B can’t solve this
  “in the early days a king rolled the stake”
  see conversation log at: https://www.signalogic.com/images/Llama-22-7B_sound-alike_error_fail.png
  exhibits typical LLM failures - incorrect answers, made up words, and circular logic
  evidently model reduction / quantization makes the problem difficult, as LLMs such as ChatGPT can easily solve it
  Llama-2 parameters:
Tested recently with Llama-3.1 8B, no change
Key point: if we refine the question, for example “which of these two word combinations is more likely” then the SLM becomes more useful. But that requires us to know a-priori what combinations to suggest
HuggingFace Llama-2 extended chat log (we changed their HTML to expand the text box vertically)

## Slide 15: Functional Requirements
Correct sound-alike errors independently of ASR model and language model
Real-time – must run every 250 to 500 msec
  minimum 10 token/sec, preferably 20
Backwards / forwards context of 3-4 tokens (words)
  eliminate need for LLM with wide context window, domain knowledge, and extensive web page training
Compliant with emerging teleoperation standards
  California included teleoperation as part of its regulation for driverless vehicles in 2018
  NIST conference in 2020
  WiFi or USB port interfaces typical
https://www.eetasia.com/why-autonomous-vehicles-will-need-teleoperation

## Slide 16: Why Not Use a GPU ?
An Nvidia Jetson Orin Nano running Llama-2 7B meets or exceeds performance and size requirements, but …
  would consume most of the 15W power consumption budget
  we still need to run RTP (i.e. codecs such as AMR or EVS), audio classification, noise removal, and ASR. These are algorithms and sequential logic, extremely difficult to code in Cuda
  we may need additional CPU cores for application-specific requirements
Needs a fan, can’t operate heat-sink only
At some point a small form-factor GPU may make sense, but first we need to develop a working system without closed source tools and dependencies

## Slide 17: Technology Overview
Conventional CPUs
  Arm, x86
  no GPUs, no HBM
Conventional memory, 8 GB min
Substantially reduce sound-alike errors
Allow training and reduction of very small, fast SLMs
  test different SLMs: Llama-2, Arcee, more
Keep the solution general
  allow any ASR model
  allow any method of language model reduction, quantization

## Slide 18: Technology Overview – Dataflow
Robotaxi
Language Translation
1 Text-to-Speech

## Slide 19: Sound-Alike Training
Database of 10,000 words run through text-to-speech
  STFT 1 generates 2-D spectrographs
  formant tracing creates simplified images
Training algorithm forms very long memory addresses (VLMAs) from images
  locates sound-alikes near each other
  maximizes distance between non-alikes
  after transformation VLMAs are non-linear
Effectively this forms a “proximity addressable memory” (PAM)
  similar to CAM (content addressable memory), but address space organization matters
  search is extremely fast
  think of it as a 3-D memory space, if you’re standing in it you can look around to see what’s near you
1 Short-Time FFT

## Slide 20: Sound-Alike Inference
With our tailored search domain, we ask the SLM “which of these possible words is more likely”
  3-4 word context window vastly reduces SLM layers and weights …
  … thus reducing processing time - 100s of SLM queries can be completed in 100 msec or less
  further decision making is possible based on multiple results, for example consensus word choice more likely to produce a safe, non-false-positive ROS command
This approach models the human brain
  it’s a given that real-time ASR models will generate errors, regardless of model, due to difficult conditions
  sound alike inference is an iterative “post-processing” stage. When someone says the word “invoice” but you hear “envoy”, it takes you some time to figure it out – this is known as Echoic Memory
  it should not be the case that we need an LLM to inference huge amounts of training text. The search domain – and the search itself – should be limited
1 https://www.nature.com/articles/s41598-019-48796-9
Echoic Memory allows for ASR correction 1

## Slide 21: Proximity Addressable Memory (PAM)
Concept has been around since 1989
  even then was intended for neural networks 1
  recent works are reviving interest 2
  a related concept is “Associative Memory” 3
Basic ideas
  weights are 1-bit, forming memory addresses
  PAM models a physical 3-D memory space with extreme emphasis on energy efficiency (minimal distance between related data), as we might expect in evolution
Advantages
  access time can be very slow, on order of msec
  errors are not a problem, no EDAC circuitry needed
  consumes milliwatts, not megawatts
Problems
  to fully emulate the brain, huge amounts of mem are required, at least Exabytes
  for now we simulate with smaller amounts and SSD paging
1 https://www.semanticscholar.org/paper/PROXIMITY-CONTENT-ADDRESSABLE-MEMORY?AN-EFFICIENT-Roberts/cc9ba91edc53903f560515c7dff6c9abf7e3f7d0
2 https://dl.acm.org/doi/10.1145/3195970.3196014
3 https://www.nature.com/articles/s41598-022-25708-y
Associative memory visualization 3

## Slide 22: Status and Next Steps
Working now
  RTP, audio classification, noise removal - one Atom core in real-time
  Kaldi ASR - one Atom core in real-time
  pico ITX board (quad core Atom x5-E3940)
  20,000 word vocabulary
Continue development
  further testing of sound-alike detection
  decide which SLM to use – two (2) cores max
  live demo with pico ITX board