## Slide 1: Autonomous Agents Networks
Akraino Physical AI Blueprint Family, v0.2

## Slide 2: Contents
Overview – Agents, Machines, and Interaction
Motivation
  autonomous agents are the next industrial revolution
  prioritize communication, collaboration, and human safety
Agent-Agent Interaction
  use cases
  cloud independent
Human-Agent Interaction
  use cases
  safety is a primary concern
Key Technologies
  P2P communication over cellular and satellite networks
  small multimodal models
    human interaction - audio and visual
    environmental recognition – hazards and dangerous conditions
    small form-factors pose performance challenges
Technology
  architecture and data flow diagrams
  messaging
  capabilities advertisement
  models
  data Storage
  authentication
Software Components
  Kaldi or Whisper ASR
  OpenCV
  Mediashark
  small multimodal models – Llama-4, Gemma 3, Qwen2, MiniPCM
Hardware Examples

## Slide 3: Overview – Agents, Machines, and Interaction
“Agents” vs “Machines”
  agents imply autonomy, goal-orientation, and ability to learn and adapt
  AAN is about physical agents
  as agents become more flexible, like humans they will be separate from machines, for example a car might have a humanoid driver (even if the car has its own automation)
  there is some risk of confusion in using the term “agents”, as “machines” will inevitably become a popular term
  specific use cases may refer to “machines”
“Interaction” includes …
  bi-directional communication, feedback
  fundamentals of collaboration – situational awareness, reaction, teamwork
  agent-agent interaction includes “M2M” standards and protocols (machine-machine communication)
Car with humanoid driver, Univ of Tokyo, Kento Kawaharazuka

## Slide 4: Motivation
In the next industrial revolution millions of agents must …
  collaborate with each other and with humans
  operate fully autonomously, with intermittent cloud connectivity when available
    expectations of always-available cloud connectivity are unrealistic, expensive, not secure, energy hungry – and most importantly – unsafe
    power outages should not immobilize AVs in the streets 2, forklifts in factories, robots helping elderly patients
  maximize energy efficiency, distributed intelligence, teamwork
    as demonstrated by evolution
Agent teamwork and human safety are top priorities
  human safety is the most difficult challenge
  teamwork leads to better decision making – “another set of eyes”, collective experience
  open source software, small form-factor hardware, new DNN1 training methods, and 3GPP and IEEE P2P communication standards are areas of emerging R&D and innovation
BigAI business models and “incompatible moats” are problematic
  they make less money when intelligence is decentralized
  not their top priority
  more difficult to recruit BigAI contributors to telecom and edge-centric blueprints
4th Industrial Revolution is the 2nd Information Revolution [Surajudeen Abiola Abdulrahman, MD, MHPM, PhD, National Health Service, UK]
4th Industrial Revolution includes human interaction with digital devices [Neos Networks, https://neosnetworks.com/resources/blog/what-is-fourth-industrial-revolution-4ir]
1 Deep Neural Network 2 https://gizmodo.com/blackout-in-san-francisco-litters-streets-with-traffic-blocking-deactivated-waymos-2000702290

## Slide 5: Autonomous Agents Networks Blueprint
AAN is a member of the Akraino Physical AI blueprint family
  agents are robots, drones, automated vehicles, factory fixed and mobile, environmental sensors
  agent-agent and human-agent interaction
  cloud independence and human safety are primary objectives
  two (2) key underlying technologies are AI and telecom
Initial use cases
  Industrial Collaboration
  Flood Detection, Prediction, and Rescue
  First Responder Machine Assistants

## Slide 6: Agent-Agent Interaction
Industrial use cases
  manufacturing
  mobile delivery and roadside (cleaning, driver assistance)
  construction
  agriculture
P2P (peer-to-peer) communication
  inter-agent (direct) using PC5 sidelink, HaLow 802.11ah, LoRa+LoRaWAN, DSRC1 IEEE 802.11x
  relay via cellular and satcom networks using C-V2X and PC5-NTN relay
  multicast to other agents in close proximity
  high MHz to mid GHz bands
    free spectrum bands, for example band formerly used by cordless phones
    C-V2X and DSRC use 5.9 GHz
    sometimes known as “mobile WiFi”
  short, low-power, codified emergency and safety messages
  optional text and low bitrate audio and video, depending on agent compute capacity
PC5 Relay
PC5 Sidelink
1 Dedicated Short Range Communications
PC5 Relay
LoRa / HaLow
LoRa / HaLow

## Slide 7: Human-Agent Interaction
Use cases
  flood prediction, detection, and rescue
  first responder machine assistants
  proximate machine safety
Audio and visual interaction
  small multimodal models
  apps supported but not required, we assume unreliable or unavailable cloud connection
  very small form-factor devices (e.g. pico ITX)
  background noise, urgent or stressed voice input, and background talkers
  machine noise from servo motor and other mechanical sources
Drawing excerpt from Amazon delivery drone patent (see Supplemental slides for more information)

## Slide 8: Key Technologies
Telecom
  P2P communications between agents, relay over cell and satellite networks
  short, energy-efficient, machine-readable messages prioritized by human safety, commercial need, machine failure, etc
  local IP, non-IP
AI
  small multimodal models, recognizing …
    speech
    behavior, and gestures
    hazards and dangerous conditions

## Slide 9: Technology Challenges
Severe SWaP 1 constraints
  small size, especially in drone and consumer applications
  low power consumption, posing a technical challenge for communication and small multimodal models
  weight is limited and may have less obvious consequences, for example GPU use may be limited due to heatsink or liquid cooling requirements
Model performance and accuracy
  limited number of CPU cores
Data storage
  dedicated storage nodes may be required
Authentication
  authenticating human-agent interaction expected to be extremely difficult problem
    potential risks include 1) “spoofing”; i.e. humans giving agents fake or harmful instructions and 2) physical obstruction or damage to agents
  agent-agent authentication
1 Size, weight, and power consumption

## Slide 10: Technology – Architecture Diagram

## Slide 11: Technology – Data Flow Diagram

## Slide 12: Technology – Messaging
Format and Prioritization
  pre-defined, machine readable, and brief to reduce power consumption
  prioritized by classification and type – emergency, safety, event, collaboration, etc.
  types may be further sub-prioritized
  optional text, audio, and video
  local IP and non-IP; public IP when a router is available
Messages contain “Action” field
  allow other agents in the P2P network to act on the message
  if they have sufficient model, storage, or authentication capabilities
Message standards
  no cross-industry standard yet
  some standards may partially apply, such as SAE J2945 series
    defines requirements for vehicle-to-vehicle safety systems, including alerts for emergency vehicles (EVA) and road hazards, using DSRC or C-V2X for interoperability
    establishes data and message protocols for real-time warnings like Emergency Vehicle Alerts (EVA) and Roadside Alerts (RSA)
Cloud and application domain communication use TCP/UDP
  HTTPS and other common protocols

## Slide 13: Technology – Messaging, cont.
Message Organization
  organized by classification, type, priority, size, content
  emergency and safety messages are short and pre-defined to minimize data rate, power consumption, and errors (e.g. giving an automated vehicle the wrong instructions)
  “Actions” field specifies handling by P2P network, for example an agent can request “Interpretation” of audio and video data by multi-modal or language models offered by another agent with advanced model capability and/or cloud connection
  optional fields use standard formats such as file attachments, SMS, MIME
No cross-industry standard for this yet
Classification | Types | Priority | Size | Message Format, Structure | Content | P2P Actions | Examples | Related Standards
Emergency | Immediate hazard or loss-of-control condition | Highest | Very Short | Fixed, predefined | Enumerated codes only, no optional fields, no free text | Multicast, Interpret, Immediate Acknowlegment, Follow-up | Emergency stop, collision imminent, flood, fire, human in danger | SAE J2735; IEC 61784-3; ETSI DENM
Safety | Developing or persistent unsafe condition | Very High | Short | Fixed, predefined | Enumerated condition types, optional numeric parameters, no free text | Multicast, Interpret, Immediate Acknowlegment, Follow-up | Flood warning, obstacle detected; unsafe proximity; degraded control | ISO 13849; IEC 61508; PROFIsafe
Event Notification | Discrete operational event | High | Medium (data rate and protocol dependent) | Structured, with optional fields for additional text, audio, and video | Required event code, optional fields using standard formats such as SMS, MIME, file attachments | Multicast, Interpret, Follow-up | Route blocked, task completed, equipment fault | ETSI CAM/DENM; OPC UA Events; DDS
Status / Awareness | Periodic situational or state updates | Medium | Short to Medium | Semi-structured, with optional fields | State vectors, counters, identifiers; no narrative text | Multicast, Interpret, Follow-up | Position update, mode change, utilization status | SAE J2945; DDS; OPC UA
Maintenance / Diagnostics | Health monitoring and service data | Medium | Medium to Large | Semi-structured, with optional fields | Diagnostic codes, key-value pairs, optional free text | Multicast, Interpret, Follow-up | Service reminder, error logs, calibration data | IEC 62541 (OPC UA); ISO 13374
Collaboration / Teamwork | Operational / functional communication | Medium | Medium to Large | Unstructured, application dependent | Instructions, follow-up, progress reports, database updates | Multicast, Interpret, Follow-up | “Please supply more of material X”, “will be offline for N hours for maintenance” | Vendor-specific; ISO/IEC 30141
Non-Critical / Bulk Data | Operational / functional communication | Low | Large | Unstructured, application dependent | Files, extended logs, datasets | Multicast, Interpret, Follow-up | Historical data, reports, reference material | Vendor-specific; ISO/IEC 30141

## Slide 14: Technology – Agents Capabilities Advertisement
Agents advertise APIs and services for …
  language and multimodal models
  data storage and database
  authentication
Agents work together to overcome disparate capabilities
  as an example, an agent may have limited on-device gesture recognition but is unable to analyze complex images
  worst case they can only record video and audio
  on-device AI and autonomous operation are the default when possible
  cloud AI is used when necessary and available
Human interaction is key to handle situations that are
  ambiguous
  urgent or unsafe
  expert guidance needed
Agents act on P2P messages based on 1) Action field contents and 2) match with their capabilities
  action field maintains history of transmission chain
“Collaborative M2M messaging” and “content aware networking” are similar concepts
Factory agents message and action flow
WiFi

## Slide 15: Technology – Multimodal and Language Models
Agents have wide range of language and multimodal model capabilities
  SWaP constraints may be prohibitive
  drones and mobile robots may have no models, or very limited ones due to few CPU cores
  some agents may have cloud connection to large models
Agents advertise model capabilities
  “I have speech-to-text, cc me with copies of message audio”

## Slide 16: Technology – Data Storage / Database
Agents may or may not have storage
  SWaP constraints may be prohibitive
  drones and mobile robots may have no SSD, limited Flash mem
Agents advertise data storage and database capabilities
  “I have storage, cc me with message copies”
  fixed or semi-mobile agents (e.g. laptops)
  larger, heavier agents (e.g. automated vehicles)

## Slide 17: Software Components
Linux
  Ubuntu, Debian, CentOS
Kaldi or Whisper ASR
OpenCV
Mediashark
  RTP media
  highly optimized for limited CPU cores
  maximize audio quality
    packet repair and frame loss concealment
    classify audio (voice, sound, noise)
    background noise removal (other talkers, servo motors, ambient environmental noise)
small multimodal models
  Llama-4, Gemma 3, Qwen2, MiniPCM

## Slide 18: Hardware Examples
Very small form-factor
  under 15 W, battery powered for 2 - 6 hours
  4 x 3”, heat sink only, no fans
Operate as small servers
  standard Linux OS (Ubuntu, Debian, etc) and command line
  Standard gcc/g++, Python, JavaScript, other standard development tools
  in the lab connect a keyboard and display
  open source development and test support
Pico ITX quad-core Atom x86 server, Ubuntu boot
Pico ITX 6-core Arm server, Debian boot

## Slide 19: Supplemental I
Additional detail

## Slide 20: Amazon Delivery Drone Patents
2016 - 2018
System for delivery drone fleet
Widely reported in technical press, in part due to somewhat humorous drawings not commonly found in patent submissions
Are speech and gesture recognition aspects of the patent enforceable ?
  not if there exists prior art for voice and gesture communication with machines
  patent must be “novel”
  patent must be “non-obvious” to people skilled in the industry
Methods and architecture of delivery system likely enforceable – although not our concern
Stanford 2015 paper
  “Results show strong agreement between participants for many interaction techniques, as when gesturing for the drone to stop. We discovered that people interact with drones as with a person or a pet, using interpersonal gestures, such as beckoning the drone closer. We detail the interaction metaphors observed and offer design insights for human-drone interactions.”
Realistic, natural human-machine communication by voice and gesture has been depicted in Sci-Fi movies going back decades. A primary example is to “2001: A Space Odyssey” in 1968
It’s reasonable to conclude that gesture and voice communication with machines exists in a variety of prior art, is obvious and not novel, and is thus not patentable
Drawing excerpts from Amazon delivery drone patents
“Drone & Me: An Exploration Into Natural Human-Drone Interaction”, Stanford CS Dept, 2015, https://hci.stanford.edu/publications/2015/gestures/paper116.pdf

## Slide 21: Supplemental II
Following slides are FYI only, from related or previous presentations

## Slide 22: Use Cases
Factory floor personnel giving urgent commands
  possibly dangerous equipment (e.g. forklifts)
  hands-free environments (e.g. food processing)
First responders communicating with disabled or disconnected robotic vehicles
  robotaxis
  cargo trucks
Language Translation
  independent of ASR model and language model

## Slide 23: Precise Command Problem
Machine-readable APIs must be precise
Minimizing false positives is crucial
Under difficult conditions, efficient open source ASRs such as Kaldi and Whisper produce "sound-alike“ errors, for example: “in the early days a king rolled the stake” which must be corrected to “in the early days a king ruled the state”
Sound-alike errors are problematic for safety and emergency situations
  Internet / cloud connection cannot be assumed. Phones may be useless
  for a robotaxi, a first responder may use a portable hand-held device and give general, conversational such as "get off the road up ahead there and shut down“
  sometimes labeled in ASR research as “substitution errors”
Prediction and decision boundary line is always hard to define 1
1 https://medium.com/@Sanskriti.Singh/an-emphasis-on-the-minimization-of-false-negatives-false-positives-in-binary-classification-9c22f3f9f73

## Slide 24: Current SLM State-of-the-Art
Currently Llama-2 7B can’t solve this
  “in the early days a king rolled the stake”
  see conversation log at: https://www.signalogic.com/images/Llama-22-7B_sound-alike_error_fail.png
  exhibits typical LLM failures - incorrect answers, made up words, and circular logic
  evidently model reduction / quantization makes the problem difficult, as LLMs such as ChatGPT can easily solve it
  Llama-2 parameters:
Tested recently with Llama-3.1 8B, no change
Key point: if we refine the question, for example “which of these two word combinations is more likely” then the SLM becomes more useful. But that requires us to know a-priori what combinations to suggest
HuggingFace Llama-2 extended chat log (we changed their HTML to expand the text box vertically)

## Slide 25: Functional Requirements
Correct sound-alike errors independently of ASR model and language model
Real-time – must run every 250 to 500 msec
  minimum 10 token/sec, preferably 20
Backwards / forwards context of 3-4 tokens (words)
  eliminate need for LLM with wide context window, domain knowledge, and extensive web page training
Compliant with emerging teleoperation standards
  California included teleoperation as part of its regulation for driverless vehicles in 2018
  NIST conference in 2020
  WiFi or USB port interfaces typical
https://www.eetasia.com/why-autonomous-vehicles-will-need-teleoperation

## Slide 26: Why Not Use a GPU ?
An Nvidia Jetson Orin Nano running Llama-2 7B meets or exceeds performance and size requirements, but …
  would consume most of the 15W power consumption budget
  we still need to run RTP (i.e. codecs such as AMR or EVS), audio classification, noise removal, and ASR. These are algorithms and sequential logic, extremely difficult to code in Cuda
  we may need additional CPU cores for application-specific requirements
Needs a fan, can’t operate heat-sink only
At some point a small form-factor GPU may make sense, but first we need to develop a working system without closed source tools and dependencies

## Slide 27: Technology Overview
Conventional CPUs
  Arm, x86
  no GPUs, no HBM
Conventional memory, 8 GB min
Substantially reduce sound-alike errors
Allow training and reduction of very small, fast SLMs
  test different SLMs: Llama-2, Arcee, more
Keep the solution general
  allow any ASR model
  allow any method of language model reduction, quantization

## Slide 28: Technology Overview – Dataflow
Robotaxi
Language Translation
1 Text-to-Speech

## Slide 29: Sound-Alike Training
Database of 10,000 words run through text-to-speech
  STFT 1 generates 2-D spectrographs
  formant tracing creates simplified images
Training algorithm forms very long memory addresses (VLMAs) from images
  locates sound-alikes near each other
  maximizes distance between non-alikes
  after transformation VLMAs are non-linear
Effectively this forms a “proximity addressable memory” (PAM)
  similar to CAM (content addressable memory), but address space organization matters
  search is extremely fast
  think of it as a 3-D memory space, if you’re standing in it you can look around to see what’s near you
1 Short-Time FFT

## Slide 30: Sound-Alike Inference
With our tailored search domain, we ask the SLM “which of these possible words is more likely”
  3-4 word context window vastly reduces SLM layers and weights …
  … thus reducing processing time - 100s of SLM queries can be completed in 100 msec or less
  further decision making is possible based on multiple results, for example consensus word choice more likely to produce a safe, non-false-positive ROS command
This approach models the human brain
  it’s a given that real-time ASR models will generate errors, regardless of model, due to difficult conditions
  sound alike inference is an iterative “post-processing” stage. When someone says the word “invoice” but you hear “envoy”, it takes you some time to figure it out – this is known as Echoic Memory
  it should not be the case that we need an LLM to inference huge amounts of training text. The search domain – and the search itself – should be limited
1 https://www.nature.com/articles/s41598-019-48796-9
Echoic Memory allows for ASR correction 1

## Slide 31: Proximity Addressable Memory (PAM)
Concept has been around since 1989
  even then was intended for neural networks 1
  recent works are reviving interest 2
  a related concept is “Associative Memory” 3
Basic ideas
  weights are 1-bit, forming memory addresses
  PAM models a physical 3-D memory space with extreme emphasis on energy efficiency (minimal distance between related data), as we might expect in evolution
Advantages
  access time can be very slow, on order of msec
  errors are not a problem, no EDAC circuitry needed
  consumes milliwatts, not megawatts
Problems
  to fully emulate the brain, huge amounts of mem are required, at least Exabytes
  for now we simulate with smaller amounts and SSD paging
1 https://www.semanticscholar.org/paper/PROXIMITY-CONTENT-ADDRESSABLE-MEMORY?AN-EFFICIENT-Roberts/cc9ba91edc53903f560515c7dff6c9abf7e3f7d0
2 https://dl.acm.org/doi/10.1145/3195970.3196014
3 https://www.nature.com/articles/s41598-022-25708-y
Associative memory visualization 3

## Slide 32: Status and Next Steps
Working now
  RTP, audio classification, noise removal - one Atom core in real-time
  Kaldi ASR - one Atom core in real-time
  pico ITX board (quad core Atom x5-E3940)
  20,000 word vocabulary
Continue development
  further testing of sound-alike detection
  decide which SLM to use – two (2) cores max
  live demo with pico ITX board